## Slide 1: GEOSYNTHETICS

## Slide 2: Content:
Concept of geosynthetics
Role of geosynthetics
Geosynthetics products
Application of geosynthetics
Geosynthetic products of natural material
Test for Geosynthetics
Advantages
Analysis of present scenario (Usage, graphs)

## Slide 3: Geosynthetics:
The term ‘Geosynthetics’ has two parts: the prefix ‘geo’, referring to an end use associated with improving the performance of civil engineering works involving earth/ground/soil and the suffix ‘synthetics’, referring to the fact that the materials are almost exclusively from man-made products. The materials used in the manufacture of geosynthetics are primarily synthetic polymers generally derived from crude petroleum oils; although rubber, fiberglass, and other materials are also sometimes used for manufacturing geosynthetics.

## Slide 4: Roles of geosynthetics :
Preventing intermixing of soil types or soil/aggregate to maintain the integrity of each material yet still allowing the free passage of liquids/gases. Commonly used in between sub-base/subgrade and around drainage materials.
Allowing fluids and gases to flow both through the plane of the material. Commonly used as components in geocomposites used for surface water runoff or for gas collection under membranes.
Restraining soil particles subject to hydraulic forces whilst allowing the passage of liquids/gases. This function is often partnered with separation e.g. in coastal defence applications or wrapped drains.
Providing additional strength to soils to enable steep slopes and soil structures to be constructed, and allow construction over weak and variable soils.

## Slide 5: Raw materials
Almost exclusively, the raw materials from which geosynthetics are produced are polymeric.
Polymers are materials of very high molecular weight and are found to have multifarious applications in the present society.
The polymers used to manufacture geosynthetics are generally thermoplastics, which may be amorphous or semi-crystalline. Such materials melt on heating and solidify on cooling. The heating and cooling cycles can be applied several times without affecting the properties.
Any polymer, whether amorphous or semi-crystalline, consists of long chain molecules containing many identical chemical units bound together by covalent bonds. Each unit may be composed of one or more small molecular compounds called monomers, which are most commonly hydrocarbon molecules.
The process of joining monomers, end to end, to form long polymer chains is called polymerization.
Manufacture of polymers is generally carried out by chemical or petrochemical companies who produce polymers in the form of solid pellets, flakes or granules.

## Slide 6: Geosynthetic products of natural material
Although most of the geosynthetics are made from synthetic polymers, a few specialist geosynthetics, especially geotextiles, may also incorporate steel wire or natural biodegradable fibres such as jute, coir, paper, cotton, wool, silk, etc.
Biodegradable geotextiles are usually limited to erosion control applications where natural vegetation will replace the geotextile’s role as it degrades. Jute nets are marketed under various trade names, including geojute, soil saver, and anti-wash.
They are usually in the form of a woven net with a typical mesh open size of about 10 by 15 mm, a typical thickness of about 5 mm and an open area of about 65%.
Vegetation can easily grow through openings and use the fabric matrix as support. The jute, which is about 80% natural cellulose, should completely degrade in about two years. An additional advantage of these biodegradable products is that the decomposed jute improves the quality of the soil for vegetation growth.

## Slide 7: Areas of Application
Environmental Protection
Land Engineering
Coastal Protection
Rock fall protection
Canal Lining
Flood Control
Infrastructure Development
Roads
Railways
Ground Improvement
Slope Stabilization

## Slide 8: Infrastructure development: Roads:
Roads often have to be constructed across weak and compressible soil subgrades. It is therefore common practice to distribute the traffic loads in order to decrease the stresses on the soil subgrade.
This is generally done by placing a granular layer over the soil subgrade. The granular layer should present good mechanical properties and enough thickness.
The long-term interaction between a fine soil subgrade and the granular layer, under dynamic loads, is likely to cause pumping erosion of the soil subgrade and penetration of the granular particles into the soil subgrade, giving rise to permanent deflections and eventually to failure.
At present, geosynthetics are being used to solve many such problems.

## Slide 9: Railways:
Railway tracks serve as a stable guide way to trains with appropriate vertical and horizontal alignment.
To achieve this role each component of the track system must perform its specific functions satisfactorily in response to the traffic loads and environmental factors imposed on the system.
Geosynthetics play an important role in achieving higher efficiency and better performance of modern-day railway track structures. They are nowadays used to correct some track support problems.
Acceptance and use of geotextiles for track stabilization is now common practice in the USA, Canada and Europe.
Geotextiles are also being used in high maintenance locations such as turnouts, rail crossings, switches and highway crossings. One of the most important areas served by geotextiles is beneath the mainline track for stabilization of marginal or poor subgrade, which can suffer from severe mud-pumping and subsidence.

## Slide 10: Slope Stabilization
In recent years geosynthetic-reinforced slopes have provided innovative and cost-effective solutions to slope stabilization problems, particularly after a slope failure has occurred or if a steeper than safe unreinforced slope is desirable. They provide a wide array of design advantages as mentioned below :
reduce land requirement to facilitate a change in grade;
provide additional usable area at toe or crest of slope;
use available on-site soil to balance earthwork quantities;
eliminate import costs of select fill or export costs of unsuitable fill;
meet steep changes in grade, without the expense of retaining walls;
eliminate concrete face treatments, when not required for surficial stability or erosion control;
provide a natural vegetated face treatment for environmentally sensitive areas;
offer a design that is easily adjustable for surcharge loadings from buildings and vehicles.

## Slide 11: Tests for geosynthetics:
UV resistance
Chemical and biological resistance
Fire resistance
Mechanical damage resistance
Toxicity
Water flow or permeability
Tensile strength
Shear resistance

## Slide 12: ADVANTAGES:
Saving in labour
Construction is easy and speedy
Easy for complicated structures
No noise pollution
Aesthetically good and eco-friendly
Reliable and easy to install
Lightweight with minimum maintenance.
Geosynthetics have low handling and overall costs.

## Slide 13: Bibliography:
BOOK :
ENGINEERING WITH GEOSYNTHETICS- TATA MCGRAW HILL PUBLICATIONS CO.PVT.LTD,NEW DELH
NET :
THE BOMBAY TEXTILE RESEARCH ASSOCIATION, Mumbai-(www.btraindia.com)
GEOFABRICS LIMITED, U.K (www.geofabrics.com)

## Slide 14
THANK YOU